## Slide 1: IOT Based Smart Restaurant Menu Using Beaglebone Black Wireless Task Interfacing of Buzzer with BB-WI
Submitted to:
Prof. Mike Aleshams
Submitted by:
Ramandeep Kaur
Group 3

## Slide 2: Content
Hardware Requirements
Software Requirements
Project Overview
  Block Diagram(Transmitter Side)
  Block Diagram(Receiver Side)
Beaglebone Black Wireless
  Specifications
  Software Compatibility
  User input/output
  Expansion Header
  Pin Diagram

## Slide 3: Content
Buzzer
  Types of Buzzer
  Features of Buzzer
Interfacing of Buzzer with BB-WI
Interfacing Communication Protocol:GPIO
Installing Library
C Code
Output
Output video
References

## Slide 4: Hardware Requirments
Beaglebone Black Wireless
Buzzer
USB Cable
Jumper Wires

## Slide 5: Software Requirements
Terminal
GNU nano editor
GCC compiler

## Slide 6: Block Diagram(Tranmitter Side)

## Slide 7: Block Diagram(Receiver Side)

## Slide 8: Beaglebone Black Wireless
Based on the extremely successful open-source Beaglebone Black hardware design, Beaglebone Black Wireless is a high-expansion, maker-focused, community-supported open hardware computer created by the BeagleBoard.org Foundation.

## Slide 9: Specifications of BB-WI
512MB DDR3 RAM
4GB 8-bit eMMC on-board flash storage
3D graphics accelerator
NEON floating-point accelerator
2x PRU 32-bit microcontroller

## Slide 10: Software compatibility of BB-WI
Debian pre-configured with Cloud9 IDE on Node.js with BoneScript library
Third-party support of Android, Ubuntu and many more upon open source Linux kernel
Non-operating-system-based peripheral support vi TI StarterWare library

## Slide 11: User input/output
Reset button
Boot button
Power button
4 user configurable LEDs; WiFi and BT enable LEDs; power LED

## Slide 12: Expansion header
65 digital I/O with general purpose I/O, SPI, I2C, PWM, CAN, UART, SD, quadrature encoders and more
7 analog inputs
Power in/out

## Slide 13: Pin Diagram of Beaglebone Black Wireless

## Slide 14: Buzzer
A buzzer or beeper is an audio signaling device, which may be mechanical ,electromechnical or piezoelectric. Typical uses of buzzers and beepers include alarm devices, timers and confirmation of user input such as a mouse click or keystroke.

## Slide 15: Types of Buzzer
There are following kinds of buzzers, based on construction:
Piezoelectric buzzers
Magnetic buzzers
Electromagnetic buzzers
Mechanical buzzers
Electromechanical buzzers

## Slide 16: Features of Buzzer
Rated Voltage: 6V DC
Operating Voltage: 4-8V DC
Rated current: <30mA
Sound Type: Continuous Beep
Resonant Frequency: ~2300 Hz
Small and neat sealed package
Breadboard and Perf board friendly

## Slide 17: Interfacing of Buzzer with BB-WI

## Slide 18: Interfacing of Buzzer with BB-WI
Red wire(+ve) of buzzer connected to 8th pin(GPIO_67) of P8 header of BB-WI.
Black wire(Ground) of buzzer connected to 2nd pin(DGND) of P8 header of BB-WI.

## Slide 19: Interfacing communication protocol:GPIO
You can configure a GPIO pin as an input or output.If a pin is unconfigured, reading from the pin configures it as an input.Writing to the pin configures it as an output.
When you write 1 to a GPIO pin,the pin outputs +3.3V. When you write 0 to the pin,or do not write anything ,the pin is grounded and output 0V.

## Slide 20: Interfacing communication protocol:GPIO

## Slide 21: SSH to Beaglebone Black Wireless
Type this command in terminal and make ssh connection to BB-WI
ssh Debian@192.168.7.2
After this, put default password “temppwd”

## Slide 22: SSH to Beaglebone Black Wireless

## Slide 23: Installing Library
Commands installing iobb library:
  mkdir development
    For creating a development folder.
  cd development
    To enter into development folder
  cd iobb
    To enter into iobb directory
  make
  make install

## Slide 24: Installing Library

## Slide 25: C code for interfacing

## Slide 26: C code for interfacing
#include<stdio.h> //This header defines various functions for perform
#include<iobb.h> //This header allows to access GPIO
int main(void)
{
iolib_init(); //For initializing the library iobb.
iolib_setdir(8, 8, DigitalOut); //Settting GPIO pin for output(8=P8 he$
while(1)
{

## Slide 27: C code for interfacing
pin_high(8, 8);
printf("Buzzer is ON \n");
iolib_delay_ms(600); //delay of 6ms
pin_low(8, 8);
printf("Buzzer Is OFF \n");
iolib_delay_ms(600); //delay of 6ms
}
iolib_free();
return(0);
}

## Slide 28: Output

## Slide 29: Output Video

## Slide 30: References:
Interfacing:
https://www.element14.com/community/community/designcenter/single-board-computers/next-genbeaglebone/blog/2019/08/15/beaglebone-black-bbb-io-gpio-spi-and-i2c-library-for-c-2019-edition#jive_content_id_How_to_Install_the_Library
Beaglebone Black Wireless:
https://beagleboard.org/blog/2016-09-26-meet-beaglebone-black-wireless
https://www.mathworks.com/help/supportpkg/beagleboneio/ug/the-beaglebone-black-gpio-pins.html#:~:text=When%20you%20read%20the%20GPIO,of%20the%20pin%20is%201%20

## Slide 31: References:
Installing the Library:
https://www.element14.com/community/community/designcenter/single-board-computers/next-genbeaglebone/blog/2019/08/15/beaglebone-black-bbb-io-gpio-spi-and-i2c-library-for-c-2019-edition#jive_content_id_How_to_Install_the_Library
Buzzer:
https://www.quisure.com/blog/faq/what-is-a-buzzer
https://www.engineersgarage.com/tech-articles/buzzers-types-transducer-indicator-piezo-magnetic/
https://components101.com/misc/buzzer-pinout-working-datasheet