## Slide 1: IoT based smart restaurant menu using BBB Wireless Testing Hardware components-Part 2
Submitted by:
Komal Preet Kaur
Group 3
Submitted to:
Prof. Mike Aleshams

## Slide 2: Tested components:
Arduino Uno and Arduino IDE
4.3’ LCD Touch Display(Nextion)
20 * 4 LCD Display
Smoke sensor and LPG sensor(MQ-2)
CO sensor and flammable gases sensor(MQ-9)
Buzzer
GSM module(SIM900)

## Slide 3: Arduino Uno
The Arduino Uno is an open-source microcontroller based on the Microchip ATmega328P microcontroller and developed by Arduino.cc
Features:
Microcontroller: ATmega328P
Operating Voltage: 5 Volts
Input Voltage: 7 to 20 Volts
Digital I/O Pins: 14 (of which 6 can provide PWM output)
UART: 1
I2C: 1
SPPI: 1
Analog Input Pins: 6
DC Current per I/O Pin: 20 mA
DC Current for 3.3V Pin: 50 mA
Flash memory: 32 KB of which 0.5 KB used by bootloader.
SRAM: 2 KB
EEPROM: 1 KB
Clock Speed: 16 MHz

## Slide 4: Arduino Uno

## Slide 5: Arduino IDE:
The open-source Arduino Software (IDE) makes it easy to write code and upload it to the board.
This software can be used with any Arduino board such as Arduino Uno, Arduino Mega etc.
Latest version of Arduino can be downloaded from https://www.arduino.cc/en/software
To Connect Uno board to a PC , an A B USB cable(printer cable) is used. The green power LED (labelled PWR) should go on.
The USB connection with the PC is necessary to program the board and not just to power it up. The Uno automatically draw power from either the USB or an external power supply.

## Slide 6: Testing of Arduino IDE and Arduino Uno
To test Arduino IDE and Arduino Uno board, we will try to run an example code provided in Arduino IDE.
Open the LED blink example sketch: File > Examples >01.Basics > Blink.

## Slide 7: Testing of Arduino IDE and Arduino Uno
Now, we will select board type as Arduino Uno and port as COM3(usually).
Now , to upload the program, first we need to compile it from arrow button available in tool bar.
Wait a few seconds – we should see the RX and TX LEDs on the Arduino board flashing. If the upload is successful, the message «Done uploading.» will appear in the status bar.
A few seconds after the upload finishes, you should see the pin 13 (L) LED on the board start to blink (in orange). It means our Arduino board is working properly.

## Slide 8: Testing of Arduino IDE and Arduino Uno: Result

## Slide 9: Read data from Uno board:
Open the Serial Monitor to look at the data which is received from the Arduino Uno board. The Serial Monitor is opened by clicking the icon to the right in the toolbar .The Serial Monitor will open a new window which will give a serial text stream of the data printed from the Arduino Board.

## Slide 10: 4.3’’ LCD Touch Display (Nextion):
Nextion is mainly applied to IoT or consumer electronics field. It is the best solution to replace the traditional LCD and LED Nixie tube. With the Nextion Editor software ,users are able to create and design their own interfaces for Nextion display.
The Nextion has a built-in ARM microcontroller that controls the display, for example it takes care of generating the buttons, creating text, store images or change the background.
The Nextion communicates with any microcontroller using serial communication at a 9600 baud rate.

## Slide 11: Basic elements of LCD touch screen

## Slide 12: Specifications of touch display:
Compatible with Raspberry Pi, Arduino and other MCUs.
480 x 272 resolution
RGB 65K real life colors
TFT monitor with integrated 4-wire resistive touch panel
Easy 4 pin interface to any TTL serial host
16M Flash memory for user application code and data
On board micro-SD card for firmware update
Viewing Area: 95.04mm (L) × 53.86mm (W)
Adjustable brightness: 0 ~ 230 nit, the adjustment interval is 1%
5V250mA power consumption
Has a built-in RTC
supports GPIOs

## Slide 13: Testing Touch LCD:
In order to test touch LCD, we can directly connect it to supply using a micro USB adaptor(5V/0.5A).
LCD will became on and a sample GUI interface can be seen.

## Slide 14: Testing touch screen LCD using Arduino
In order to test our LCD touch screen, I have taken example of a simple GUI and shown how Arduino can communicate with this GUI by transferring data serially using UART.
Nextion editor is used to create simple GUI
Arduino IDE is used to communicate and control touch LCD.

## Slide 15: Connecting touch LCD to Arduino:
Connecting the Nextion display to the Arduino is very straightforward.
We just need to make four connections: GND, RX, TX, and +5V. These pins are labeled at the back of display.

## Slide 16: Connecting touch LCD to Arduino:

## Slide 17: Connecting touch LCD to Arduino:

## Slide 18: Creating a simple GUI :Using Nextion editor
We can download Nextion editor from https://nextion.itead.cc/
After launching it, we can see an interface like this.

## Slide 19: Overview of different sections:
Main Menu
Canvas – this is where we add our components to build the User Interface.
Toolbox – this is where we have a wide variety of components we can add to the user interface, like pictures, progress bar, buttons, sliders, and much more.
Picture/Fonts list – this shows the fonts and pictures imported to our projects. Here you can also add new fonts and pictures.
Page area – we can manage our pages here, like add more pages, copy and delete pages.
Attributes area – this part shows our component’s attributes. We can edit the component’s attributes here.
Compiler output window – this will show any errors occurred during compiling.
Event window – here we can add code to be run when an event is met.

## Slide 20: Creating a simple GUI
Clicked on new project and selected my device
and selected display direction

## Slide 21: Display direction : horizontal

## Slide 22: Creating a simple GUI After this, imported a simple .HMI file which consists of two pages ,one slider, several text boxes and buttons.
Page 0
Page 1

## Slide 23: Creating a simple GUI: compiling and uploading code to display
Click the Compile button in the main menu;
Insert the microSD card on your computer;
Go to File > Open Build Folder;
Copy the .TFT file corresponding to the file you’re currently working;
Paste that file in the microSD card
Insert the microSD card on the Nextion display and plug power.
After code is uploaded successfully, GUI is visible on display .

## Slide 24
When it is ready, it should display the following screen

## Slide 25: Creating a simple GUI
Uploading code on Arduino:

## Slide 26: Code for touch LCD:
Sending to the display requires an understanding of the Nextion instruction set and what the display expects to receive. t0.txt="Your text here"0xff 0xff 0xff This is typical of any instruction, text or data, sent to the display. The display expects 0xff 0xff 0xff to indicate the end of the instruction.
For example: Following code put page number in place of t0
void HMI_display_page(uint8_t page) { Serial.print(F("t0.txt="")); Serial.print(F("This is page ")); Serial.print(page); Serial.print("""); Serial.write(0xff); Serial.write(0xff); Serial.write(0xff); }

## Slide 27: Code for touch LCD:
Min loop contains two functions:
HMI_read();
clock_run();
HMI_read() : HMI_read takes the data sent from the Nextion to the serial port and processes it depending on what has been sent
There are 3 levels of nested switch statements corresponding to the page, the type of object and the index of the object.
clock_run() : creates a real time clock using millis() function as the timing source.

## Slide 28: Testing of touch LCD: output
Here is link of testing video:
https://youtu.be/5cyeuH_8Kpw

## Slide 29: Testing 20 * 4 LCD Display
This LCD with an I2C port is developed to solve the multiple IOs problem. It is also simple to handle. It has only two bidirectional data lines, a serial data line and a serial clock one. Specifications: Display: 4 lines x 20 characters Backlight: blue with white character color LCD controller: HD44780 Pin Definition: VCC/ GND/SDL and SCA Contrast Adjust: Potentiometer Backlight Adjust: Jumper Default Address: 0x27 Working Voltage: 5V Application: Used to display Characters, letters and Numbers

## Slide 30: Pin Description of LCD:

## Slide 31: I2C LCD Connections

## Slide 32: I2C LCD with Arduino wiring diagram

## Slide 33: Installing libraries and code for LCD :
LiquidCrystal_I2C library need to be installed. This library has many built-in functions that make programming the LCD quite easy.
The LiquidCrystal_I2C library works in combination with the Wire.h library which allows to communicate with I2C devices.
The library does include some examples that we can use, but we will have to modify them to match hardware setup.
I have used HelloWorld example to test my LCD

## Slide 34: HelloWorld code:

## Slide 35: LCD Testing : Output

## Slide 36: Testing of CO sensor:
Gas Sensor(MQ9) module is useful for gas leakage detection (in home and industry).
It is suitable for detecting CO, CH4.
Due to its high sensitivity and fast response time, measurements can be taken as soon as possible.
The sensitivity of the sensor can be adjusted by using the potentiometer.
The output voltage from the Gas sensor increases when the concentration of gas increases.

## Slide 37: Specifications:

## Slide 38: CO sensor: working
It uses the sensitive material SnO2, which have lower conductivity in clean air.
It make detection by method of cycle high and low temperature, and detect CO when temperature is low(heated by 1.5V).
The sensors conductivity is more higher along with the gas concentration rising. When temperature is high (heated by 5.0V), it detects Methane, Propane etc. combustible gas and cleans the other gases absorbed under low temperature.
MQ-9 gas sensor has high sensitivity to Carbon Monoxide, Methane and LPG.

## Slide 39: Pin description of MQ-9:
In Module:
Here H pins are two sides of heating element SnO2. one pin is connected to Vcc ,other to GND
A pins and B pins are shorted internally and are input and output pins.

## Slide 40: Connection diagram of MQ-9 and Arduino

## Slide 41: Code for Arduino:

## Slide 42: Code description
float sensor_volt;
float sensorValue;
sensorValue = analogRead(A0);
sensor_volt = sensorValue/1024*5.0;
Serial.print("sensor_volt = ");
Serial.print(sensor_volt);
Serial.println("V");
delay(1000);
It is a simple code to read analog voltage from sensor using
sensorValue = analogRead(A0);
Then sensor value is converted to voltage using a standard calculation obtained by simple network calculations Rs=(Vc/VRL-1)×RL.

## Slide 43: Output at serial monitor:

## Slide 44: Testing of CO sensor:
This output is obtained when sensor is tested in open air.
This sensor requires a pre heating time of about 24-48hours.
It shows an output voltage for which, which can be used as a threshold to detect any increase/decrease in gas concentration.

## Slide 45: Testing of smoke sensor:
MQ2 is one of the commonly used gas sensors in MQ sensor series.
It is a Metal Oxide Semiconductor (MOS) type Gas Sensor also known as Chemiresistors as the detection is based upon change of resistance of the sensing material when the Gas comes in contact with the material.
Using a simple voltage divider network, concentrations of gas can be detected.
The sensor is actually enclosed in two layers of fine stainless steel mesh called Anti-explosion network. It ensures that heater element inside the sensor will not cause an explosion, as we are sensing flammable gases.

## Slide 46: Specifications:

## Slide 47: Pin description of smoke sensor:

## Slide 48: Connection diagram:

## Slide 49: Code:

## Slide 50: Code explanation:
The sketch starts by defining Arduino pin to which analog
pin of MQ2 gas sensor is connected. A variable called sensorValue is also defined to store sensor value.
#define MQ2pin (0)
float sensorValue; //variable to store sensor value
In setup function: we initialize serial communications with the PC and wait for 20 seconds to allow sensor to warm up.
Serial.begin(9600); // sets the serial port to 9600
Serial.println("Gas sensor warming up!");
delay(20000); // allow the MQ-6 to warm up

## Slide 51: Code explanation: contd…
In loop function: the sensor value is read by analogRead() function and displayed on serial monitor.
sensorValue = analogRead(MQ2pin); // read analog input pin 0 Serial.print("Sensor Value: ");Serial.print(sensorValue);
When the gas concentration is high enough, the sensor usually outputs value greater than 300. We can monitor this value using if statement. And when the sensor value exceeds 300, we will display ‘Smoke Detected!’ message.
if(sensorValue > 300)
{
Serial.print(" | Smoke detected!");
}

## Slide 52: Output on serial monitor

## Slide 53: Output video:
https://youtu.be/hqwMIpaMD4M

## Slide 54: Testing Buzzer: description
In a magnetic buzzer, a current is driven through a coil of wire which produces a magnetic field. A flexible ferromagnetic disk is attracted to the coil when the current is present and returns to a "rest" position when the current is not flowing through the coil.
the sound from a magnetic buzzer is produced by the movement of the ferromagnetic disk in a similar manner to how the cone in a speaker produces sound.
A magnetic buzzer is a current driven device, but the power source is typically a voltage.
The current through the coil is determined by the applied voltage and the impedance of the coil.

## Slide 55
Working of buzzer:
The vibrating disk in a magnetic buzzer is attracted to the pole by the magnetic field. When an oscillating signal is moved through the coil, it produces a fluctuating magnetic field which vibrates the disk at a frequency equal to that of the drive signal.

## Slide 56: Schematic of buzzer interfacing:

## Slide 57: Code for buzzer:
const int buzzerPin = 9; // declaring the PWM pin</p><p>
void setup()
{
Serial.begin(9600);
pinMode(buzzerPin, OUTPUT);
void loop()
{
tone(buzzerPin, 50);
delay(500);
noTone(buzzerPin);
delay(1000);
}

## Slide 58: Connection diagram:
Output video link:
https://youtu.be/H97Wd-TixSA

## Slide 59: GSM module –SIM900
GSM stands for Global System for Mobile
Communications and is the global standard for mobile communications.
GPRS stands for General Packet Radio Service. GPRS is a mobile service on the 2G and 3G cellular communication.
Compatible with Arduino and clones
Based on SIM900 module from SIMCOM
Allows you to send SMS, MMS, GPRS and Audio via UART using AT commands.
It has 12 GPIOs, 2 PWMs and buit-in ADC of the SIM900 module
Quad Band: 850; 900; 1800 and 1900 MHZ, so it should work in all countries with GSM (2G) networks
Control via AT commands
Supports RTC (real time clock) – it has a holder for a 3V CR1220 battery at the back
Has microphone and headphone jacks for phone calls

## Slide 60: On-board components of GSM Module:

## Slide 61: Steps to configure a module:
Insert the SIM card into the SIM card holder
On the serial port select, make sure the jumper cap is connected to use software serial.
Power the shield using an external 5V power supply. Make sure to select the external power source with the toggle switch next to the DC jack.
Then, the Status LED will light up and the NetLight LED will blink every 800 ms until it finds the network. When it finds the network, the NetLight LED will start blinking every three seconds.

## Slide 62: Connection diagram:

## Slide 63: References:
Arduino Uno:
https://en.wikipedia.org/wiki/Arduino_Uno
https://www.arduino.cc/en/Guide/ArduinoUno
https://www.narom.no/undervisningsressurser/the-cansat-book/the-primary-mission/software-start-up-and-test-of-arduino-uno/
Nextion touch display:
https://pl.aliexpress.com/item/32874330873.html
https://nextion.tech/datasheets/nx4827t043/
https://randomnerdtutorials.com/nextion-display-with-arduino-getting-started/
https://forum.arduino.cc/index.php?topic=604185.0

## Slide 64
Gas Sensor(MQ9) :
https://wiki.seeedstudio.com/Grove-Gas_Sensor-MQ9/
https://www.elecrow.com/wiki/index.php?title=Analog_CO/Combustible_Gas_Sensor(MQ9)
https://www.instructables.com/Arduino-CO-Monitor-Using-MQ-7-Sensor/
20 *4 LCD Module specifications:
https://www.amazon.ca/gp/product/B07TXGD3WS/ref=ppx_od_dt_b_asin_title_s00?ie=UTF8&psc=1
https://www.makerguides.com/character-i2c-lcd-arduino-tutorial/
Smoke sensor:
https://lastminuteengineers.com/mq2-gas-senser-arduino-tutorial/

## Slide 65
Buzzer
https://www.cuidevices.com/product-spotlight/piezo-and-magnetic-buzzers#:~:text=Working%20Principle%20of%20Magnetic%20Buzzers,that%20of%20the%20drive%20signal.
https://www.cuidevices.com/blog/buzzer-basics-technologies-tones-and-driving-circuits
https://www.instructables.com/Interfacing-Buzzer-to-Arduino/
GSM SIM900
https://randomnerdtutorials.com/sim900-gsm-gprs-shield-arduino/