## Slide 1: Xbee(transmitter) Interfacing with BBB wireless
Submitted by
Ashok Kumar Saini(c0762216)

## Slide 2: What is Xbee?
XBee S2C is a RF module designed for wireless communication or data exchange and it works on ZigBee mesh communication protocols that sit on top of IEEE 802.15. 4 PHY.
The module provides wireless connectivity to end-point devices in any ZigBee mesh networks including devices from other vendors.

## Slide 3: Pin Diagram of Xbee
z

## Slide 4: Pin Configuration of Xbee
Pin | Name | Description
1 | VCC | Power supply
2 | DOUT/DIO13 | UART data out pin (TXD)/GPIO
3 | DIN/CONFIG / DIO14 | UART data in pin (RXD)/ GPIO
4 | DIO12/SPI_MISO | GPIO/ Master Input-Slave Output pin of SPI interface
5 | RESET | Module Reset pin
6 | RSS PWM /DIO10 | RX Signal Strength Indicator pin / GPIO
7 | PWM1/DIO11 | Pulse Width Modulator/GPIO

## Slide 5: Pin Configuration of Xbee
Pin | Name | Discription
8 | RESERVED | Do not connect
9 | DTR/SLEEP_RQ/ DIO8 | Pin Sleep Control line /GPIO
10 | GND | Ground
11 | DIO4/ SPI_MOSI | GPIO/Master Output-Slave Input pin of SPI interface
12 | CTS/DIO7 | Clear-to-send flow control/GPIO
13 | ON_SLEEP/DIO9 | Device status indicator/GPIO
14 | VREF | Voltage Reference for ADC

## Slide 6: Pin Configuration of Xbee
Pin | Name | Discription
15 | ASC/DIO5 | Associate Indicator/GPIO
16 | RTS/DIO6 | Request to send flow control/ GPIO
17 | AD3/DIO3/SPI_SSEL | Analog input/GPIO/SPI slave select
18 | AD2 /DIO2/SPI_CLK | Analog input/GPIO/SPI clock
19 | AD1/DIO1/SPI_ATTN | Analog input/GPIO/SPI attention
20 | AD0/DIO0/C | Analog input/GPIO/ Commissioning button

## Slide 7: Features and Electrical Characteristic of Xbee
Transmission Frequency: 2.4GHz to 2.5GHz
Number of Channels: 16 Direct Sequence Channels
Featured with UART (250 Kb/s maximum) and SPI (5 Mb/s maximum) interface
Featured with software adjustable transmitting power
Indoor/Urban Range: 200ft
Outdoor RF line-of-sight Range: up to 4000ft
Transmit Power Output: 6.3mW (8dBm) in Boost mode,2mW (3dBm) in Normal mode

## Slide 8: Features and Electrical Characteristic of Xbee
Receiver Sensitivity: -102dBm in Boost mode, -100dBm in Normal mode
Supply Voltage Range: +2.1V to +3.6V
Operating Current: 33mA (at3.3V, for Normal mode) , 45mA (at 3.3V,for Boost mode)
Idle Current: 9mA
Maximum output current on all pins together: 40mA
Power-down Current: <1uA @25C
ESD protection: 3000V
Operating Temperature: -40ºC to 85° C

## Slide 9: Need of Xbee module !
As our project has two isolated part (transmitter/receiver ). We need to send Data from one part to other.
Xbee provides sufficient data rate (250Kbps).
Simplicity in configuration and interfacing with microcontrollers.
A single XBee module does not have much use unless you already have a ZigBee mesh network up and running. So if there is no mesh network working you need at least two modules for establishing wireless communication.

## Slide 10: UART interfacing of Xbee

## Slide 11: UART interfacing of Xbee

## Slide 12: Software used for Xbee- XCTU
XCTU is a free, multi-platform application compatible with Windows, MacOS and Linux
Graphical Network View for simple wireless network configuration and architecture
API Frame Builder is a simple development tool for quickly building XBee API frames
Firmware Release Notes Viewer allows users to explore and read firmware release notes

## Slide 13: XCTU software

## Slide 14: Configuring Xbee
PAN ID- Assign same for Both Xbees
MAC address (16 bits)
Xbee1 -> 0013A20041D157C6
Xbee2 -> 0013A20041D18631
High
Low
Node Identifier
CE Coordinator Enable

## Slide 16: Xbee configuration as transmitter

## Slide 17: Xbee Configuration as Receiver

## Slide 18: Pin Diagram of BBB wireless

## Slide 19: Interfacing with BBB wireless
Connect pin 1 of Xbee to pin4 0f BBB wireless (P9 Header)
Connect pin 10 of Xbee to Pin 46 of BBB wireless (P9 header )
Connect pin 2 of Xbee to pin26 0f BBB wireless (P9 Header)
Connect pin 3 of Xbee to Pin 24 of BBB wireless (P9 header )

## Slide 21: Interfacing with Arduino
Connect pin 1 of Xbee to 3.3V 0f Arduino uno wireless
Connect pin 10 of Xbee to GND Arduino uno
Connect pin 2 of Xbee to Tx of Arduino uno
Connect pin 3 of Xbee to Rx of Arduino uno

## Slide 23: UART interfacing of Xbee using C
Add kernel Libraries
Save USB locations of Devices
Give Commands to Communicate with other Xbee

## Slide 25: UART interfacing of Xbee using python
import Adafruit_BBIO.UART as uart
uart.setup('UART1')
import serial
xbee=serial.Serial(port="/dev/ttyO1", 9600, timeout=1)
while(1):
  print(xbee.readline())
xbee.write('From Beaglebone')

## Slide 28: Reference
Xbee configuration
https://components101.com/wireless/xbee-s2c-module-pinout-datasheet#:~:text=XBee%20S2C%20is%20a%20RF,including%20devices%20from%20other%20vendors.
XCTU software
https://www.digi.com/products/embedded-systems/digi-xbee/digi-xbee-tools/xctu#productsupport-utilities

## Slide 29: Reference
Interfacing of xbee
https://stackoverflow.com/questions/tagged/beagleboneblack?sort=votes&page=4
https://medium.com/@ing.david.mata/in-this-tutorial-i-am-going-to-show-you-how-you-can-send-data-wirelessly-between-an-arduino-to-a-cb18cac1c984

## Slide 30: Questions? Thanks
z